## Slide 1: Shutter Speed
&
Aperture

## Slide 2: Exposure
Exposure Explained
The very beginning
Overexposure—too much light
Underexposure—not enough light

## Slide 3: Exposure = Aperture + Shutter Speed
What is Exposure?
What affects Exposure?
How do they affect Exposure?
What happens when they are misaligned?
And ONE MORE VIDEO on exposure. (yeah!?)

## Slide 4: ISO
ISO Explained
It is your film’s sensitivity
to light
100 ISO has the highest
quality
3200 ISO is appropriate for sports
100 or 200 ISO would need a tripod indoors

## Slide 5: Shutter Speed
How long the shutter stays open to take the photograph.
How the shutter works….

## Slide 6: Shutter Speed on our cameras…
On a Manual SLR camera
The shutter is changed by spinning the dial
Speeds on this camera: 1/1000, 1/500, 1/250, 1/125, 60, 30, 15, 8, 4, 2, B
On a Digital SLR camera
On a Digital SLR (Nikon D3000)
Set the camera to Manual (M)
Spin the dial
Speeds on this camera: 30 sec-1/4000
Notes: *mention point & shoot

## Slide 7
Slow Shutter Speed (1/30 or slower)

## Slide 8
Using a Fast Shutter Speed (1/250 or higher)

## Slide 9: You can try to show or stop motion while your camera is an automatic mode…
Night Photo Option
to show motion
Sports Photo Option
to freeze motion

## Slide 10: Aperture
Aperture is the opening through which light travels—the
size of the opening dictates the amount of light allowed in.

## Slide 11
How the Aperture works…
Depth of Field Explained
Watch these videos to further explore aperture and depth of field.

## Slide 12
Large Aperture opening = Shallow Depth of Field
f1.8, f2, f2.8, f4, f5.6
*the smaller the number, the larger the opening*

## Slide 13
Small Aperture Opening = Large Depth of Field
f8, f11, f16, f22
*the larger the number, the smaller the opening*

## Slide 14: Aperture on our cameras…
On a Manual SLR camera
The aperture is changed by turning the ring so that the Fstop lines up with the red-oragne line
Fstops: f1.7, f2.8, f4, f5.6, f8, f11, f16
On a Digital SLR camera
On a Digital SLR (Nikon D3000)
Set the camera to Manual (M)
Hold the exposure button & spin the dial
Fstops: f5, f5.6, f6.3, f7.1, f8, f9, f10, f11, f13, f14, f16, f18, f20
Notes: *mention point & shoot

## Slide 15: The Light Meter
Nikon D3000
This is the menu which shows on the screen. In the middle you see a graph from + to –.
Proper exposure is achieved when the small lines are exactly in the middle.
Far to the left creates an overexposed image. Far to the right creates an underexposed image.

## Slide 16: The Light Meter cont’d.
Our Pentax cameras have a wand that moves up and down as you change your settings. You want the wand to be in the middle and pointing straight out into the frame.

## Slide 17: Now you try!
Follow the directions on the handout while using the Camera Simulator